## Slide 1: Module 2 – GeoBIM and Planning/Building Permits –
Lars Harrie
Lund University, Sweden
Claire Ellul
University College London, UK
Notes: SLIDE 10 AND SLIDE 15 – PUT ARCSENE MAPS!!!!

## Slide 2: Main sources
https://3d.bk.tudelft.nl/projects/eurosdr-geobim/
Noardo, F., Ellul, C., Harrie, L., Olsson, P., Arroyo Ohori, K., Stoter, J. (2019). EuroSDR GeoBIM project: a study in Europe on how to use the potentials of BIM and geo data in practice. 3DGeoInfo2019 Conference, Singapore - International Archives of the Photogrammetry, Remote Sensing & Spatial Information Sciences IV-4(W8) 2019. https://doi.org/10.5194/isprs-archives-XLII-4-W15-53-2019

## Slide 3
Workflow
Sequence
https://3d.bk.tudelft.nl/projects/eurosdr-geobim/
https://3d.bk.tudelft.nl/projects/eurosdr-geobim/WorkflowDescription.pdf

## Slide 4: Other sources
Detailed delivery specifications for Geodata BIM
https://www.smartbuilt.se/projekt/informationsinfrastruktur/leveransspecifikationer/ (in Swedish)
OLSSON P.O., JOHANSSON T., ERIKSSON, H., LITHÉN T., BENGTSSON, L.-H., AXELSSON, J.ROOS, U., NELAND, K., RYDÉN, B., HARRIE, L., 2019.
Unbroken digital data flow in the built environment process - a case study in Sweden, Int. Arch. Photogramm.
Remote Sens. Spatial Inf. Sci., XLII-2/W13, 1347-1352, 2019
https://doi.org/10.5194/isprs-archives-XLII-2-W13-1347-2019. ISPRS Geospatial Week 2019, Enschede, June 10-14, 2019.
Several research projects – see references in the slides and the reading list
Some production systems and prototypes

## Slide 5: Steps in the process
0) Site selection for investors – use GeoBIM to find out the potential of a site
1) Applicants asks for new building
2) Pre-consultation and preliminary analysis
3) Building information modelling
4) Application submission
5) Application reviewed (formal)
6) Conversion to CityGML
7) Application reviewed (content requirements)
8) Building permission issuing & start of construction works
9) Inspections during the works
10) Refinements or changes throughout construction process
11) Completion of the works & building authorities notification
12) As-built IFC formal review (validation)
13) Final inspection
14) Completion certificate / use permit issuing & 3D city model update & storage of BIMs
15) Handover to asset management

## Slide 6: 1) Applicants asks for new building
This presentation deals with the process of designing and constructing a new building.
The process is different for permissions for extensions/changes in buildings, etc.

## Slide 7: Steps in the process
0) Site selection for investors – use GeoBIM to find out the potential of a site
1) Applicants asks for new building
2) Pre-consultation and preliminary analysis
3) Building information modelling
4) Application submission
5) Application reviewed (formal)
6) Conversion to CityGML
7) Application reviewed (content requirements)
8) Building permission issuing & start of construction works
9) Inspections during the works
10) Refinements or changes throughout construction process
11) Completion of the works & building authorities notification
12) As-built IFC formal review (validation)
13) Final inspection
14) Completion certificate / use permit issuing & 3D city model update & storage of BIMs
15) Handover to asset management

## Slide 8: 2) Pre-consultation and preliminary analysis

## Slide 9: Requirement of national specifications for 3D city models
Source: Blaauboer et al. (2014)
The Netherlands
3D IMGeo-CityGML
Sweden
CityGML Sve-Test
Source: Eriksson et al. (2020)

## Slide 10: Limitations of importing geodata (City model data) to BIM tools
Revit
Generally, BIM tools cannot import
point and line object, and there are some
limitations on surface objects. BIM tools
are built for volumetric objects (as used in
the figures here).
Source: Detailed delivery specification for geodata-BIM

## Slide 11: Regulations can be found in many planning instruments that varies between countries. Example UK: A landscape and townscape context plan
Source:
Exeter City Council

## Slide 12: In this presentation we use: Detail development plans
Source: Helsingborg stad

## Slide 13: Digitalisation of detail development plans
An increasing number of countries require digital detail development plans.
Ongoing work to digitalise older paper plans.
Source: Kim et al. (2019): Visual language approach to representing
KBimCode-based Korea building code sentences for automated rule checking
Also digitalisation
of building rules
are required

## Slide 14: Import of digital detail development plan into BIM environment
Plan converted into
IFC and viewed in
Solibri Model Viewer
Source: van Berlo et al. (2013)

## Slide 15
Service in Norway
Applicant analysis before application
https://bygglett.catenda.com/nysak

## Slide 16: Applicant analysis before application
http://fjl.gis.lu.se/
Prototype service created by Roger Groth, LU

## Slide 17: Steps in the process
0) Site selection for investors – use GeoBIM to find out the potential of a site
1) Applicants asks for new building
2) Pre-consultation and preliminary analysis
3) Building information modelling
4) Application submission
5) Application reviewed (formal)
6) Conversion to CityGML
7) Application reviewed (content requirements)
8) Building permission issuing & start of construction works
9) Inspections during the works
10) Refinements or changes throughout construction process
11) Completion of the works & building authorities notification
12) As-built IFC formal review (validation)
13) Final inspection
14) Completion certificate / use permit issuing & 3D city model update & storage of BIMs
15) Handover to asset management

## Slide 18: 3) Building information modelling

## Slide 19: Steps in the process
0) Site selection for investors – use GeoBIM to find out the potential of a site
1) Applicants asks for new building
2) Pre-consultation and preliminary analysis
3) Building information modelling
4) Application submission
5) Application reviewed (formal)
6) Conversion to CityGML
7) Application reviewed (content requirements)
8) Building permission issuing & start of construction works
9) Inspections during the works
10) Refinements or changes throughout construction process
11) Completion of the works & building authorities notification
12) As-built IFC formal review (validation)
13) Final inspection
14) Completion certificate / use permit issuing & 3D city model update & storage of BIMs
15) Handover to asset management

## Slide 20: 4) Application submission

## Slide 21: Model View Definition (MVD) – Formal subset of an IFC model. Example: Singapore

## Slide 22: Steps in the process
0) Site selection for investors – use GeoBIM to find out the potential of a site
1) Applicants asks for new building
2) Pre-consultation and preliminary analysis
3) Building information modelling
4) Application submission
5) Application reviewed (formal)
6) Conversion to CityGML
7) Application reviewed (content requirements)
8) Building permission issuing & start of construction works
9) Inspections during the works
10) Refinements or changes throughout construction process
11) Completion of the works & building authorities notification
12) As-built IFC formal review (validation)
13) Final inspection
14) Completion certificate / use permit issuing & 3D city model update & storage of BIMs
15) Handover to asset management

## Slide 23: 5) Application reviewed (formal)

## Slide 24: Formal checking of a BIM (IFC) file in BIM modeling checking tool
Source: Solibri.wordpress.com

## Slide 25: Checking elements according to MVD in an ETL-tool
IfcSite required
Custom transformer that reads
template file and check values.
Source: Detailed delivery specification for geodata-BIM

## Slide 26: Steps in the process
0) Site selection for investors – use GeoBIM to find out the potential of a site
1) Applicants asks for new building
2) Pre-consultation and preliminary analysis
3) Building information modelling
4) Application submission
5) Application reviewed (formal)
6) Conversion to CityGML
7) Application reviewed (content requirements)
8) Building permission issuing & start of construction works
9) Inspections during the works
10) Refinements or changes throughout construction process
11) Completion of the works & building authorities notification
12) As-built IFC formal review (validation)
13) Final inspection
14) Completion certificate / use permit issuing & 3D city model update & storage of BIMs
15) Handover to asset management

## Slide 27: 6) Conversion to CityGML

## Slide 28: Example of workflow in the conversion
Source: Donkers et al. (2015)

## Slide 29: Geometric transformation
Sjors Donkers TU Delft MSc Dissertation:
Source: Nagel et al. (2009)
Challenges -
Different geometric
representations:
CityGML – B-rep
IFC – CSG, B-rep,
SweptSolid, etc.

## Slide 30: Semantic mapping
Sjors Donkers TU Delft MSc Dissertation:
El-Mekawy et al. (2011)

## Slide 31: Example of study of conversion
A triple
graph approach
Source: Stouffs et al. (2018)

## Slide 32: More on implementation of conversion tools will follow in module 4 (in the GeoBIM benchmark)

## Slide 33: Steps in the process
0) Site selection for investors – use GeoBIM to find out the potential of a site
1) Applicants asks for new building
2) Pre-consultation and preliminary analysis
3) Building information modelling
4) Application submission
5) Application reviewed (formal)
6) Conversion to CityGML
7) Application reviewed (content requirements)
8) Building permission issuing & start of construction works
9) Inspections during the works
10) Refinements or changes throughout construction process
11) Completion of the works & building authorities notification
12) As-built IFC formal review (validation)
13) Final inspection
14) Completion certificate / use permit issuing & 3D city model update & storage of BIMs
15) Handover to asset management

## Slide 34: 7) Application reviewed (content requirements)

## Slide 35: 7) Application reviewed (content requirements)

## Slide 36: What is required for building permit rule checking?
 | BIM data | Geospatial data | BIM & Geospatial data | Total
Quantitative | 25% | 30% | 30% | 85%
Visual | 2% | 1% | 2% | 5%
Qualitative | - | - | - | 10%
Study of the Swedish regulations defined by the National Board of Housing and Planning
Quantitative – BIM data |  | Roof pitch (degree)
Quantitative – Geospatial data | Slope of the ground (gradient) | 
Quantitative – BIM and geospatial data | Building heights (m) and densification levels (total building footprint area divided by real estate area) | 
Visual BIM data | Configuration of windows should follow certain characteristics | 
Visual Geospatial data | Configuration of property units | 
Visual BIM and geospatial data | General maintenance of the character in a built-up area | 
Qualitative | Maintenance of specific historical and artistic values | 
Example for each category
Source: Olsson et al. (2018)

## Slide 37: (Semi-) Automated building permit rule checking
Source: Detailed delivery specification for geodata-BIM

## Slide 38: (Semi-) Automated building permit rule checking
Source: Detailed delivery specification for geodata-BIM

## Slide 39: Controlling building heights
Source: Olsson et al. (2018)

## Slide 40: Architecture of an ETL-script developed to calculate building area
Source: Olsson et al. (2018)

## Slide 41: Checking regulations in BIM tools (Solibri)
Source: van Berlo et al. (2013)

## Slide 42: Steps in the process
0) Site selection for investors – use GeoBIM to find out the potential of a site
1) Applicants asks for new building
2) Pre-consultation and preliminary analysis
3) Building information modelling
4) Application submission
5) Application reviewed (formal)
6) Conversion to CityGML
7) Application reviewed (content requirements)
8) Building permission issuing & start of construction works
9) Inspections during the works
10) Refinements or changes throughout construction process
11) Completion of the works & building authorities notification
12) As-built IFC formal review (validation)
13) Final inspection
14) Completion certificate / use permit issuing & 3D city model update & storage of BIMs
15) Handover to asset management

## Slide 43: Steps in the process
0) Site selection for investors – use GeoBIM to find out the potential of a site
1) Applicants asks for new building
2) Pre-consultation and preliminary analysis
3) Building information modelling
4) Application submission
5) Application reviewed (formal)
6) Conversion to CityGML
7) Application reviewed (content requirements)
8) Building permission issuing & start of construction works
9) Inspections during the works
10) Refinements or changes throughout construction process
11) Completion of the works & building authorities notification
12) As-built IFC formal review (validation)
13) Final inspection
14) Completion certificate / use permit issuing & 3D city model update & storage of BIMs
15) Handover to asset management

## Slide 44: 14) Completion certificate / use permit issuing & 3D city model update & storage of BIMs

## Slide 45: Geometric evaluation of CityGML model derived from BIM models
Source: Sun et al. (2019)

## Slide 46: General validation of geometries
Source: Ledoux H. (2018). val3dity: validation of 3D GIS primitives according to the international standardsOpen Geospatial Data, Software and Standards (2018) 3:1
https://doi.org/10.1186/s40965-018-0043-x
3D primitives validated
by val3dity

## Slide 47: Version management in the update process
Source: Eriksson et al. (2020)

## Slide 48: Steps in the process
0) Site selection for investors – use GeoBIM to find out the potential of a site
1) Applicants asks for new building
2) Pre-consultation and preliminary analysis
3) Building information modelling
4) Application submission
5) Application reviewed (formal)
6) Conversion to CityGML
7) Application reviewed (content requirements)
8) Building permission issuing & start of construction works
9) Inspections during the works
10) Refinements or changes throughout construction process
11) Completion of the works & building authorities notification
12) As-built IFC formal review (validation)
13) Final inspection
14) Completion certificate / use permit issuing & 3D city model update & storage of BIMs
15) Handover to asset management